Marine Science facilities Hurricane Emergency Plan

(8/21/08)

In the event that a hurricane warning is issued we will:
 
1.   Remove or otherwise secure movable objects around the building.
 
2.   Fill outside fiberglass tanks with water.
 
3.   Empty outside concrete holding tank and leave gate valve open.
 
4.   Turn off fresh water supply to outside and dock outlets. Open spigots and allow system to drain. Bring in all water hoses. Allow salt water lines outside to drain.
 
5.   Turn off power supply to dock at breaker box in the electrical room of the building.
 
6.   Move the truck and the van to higher ground on campus.
 
7.   Shutter windows facing the marsh with plywood or heavy tarps.
 
8.   Release all live specimens from aquaria and holding tanks. Drain inside holding tank in wet lab, turn off filter pump and secure glass aquaria in the wet-lab.
 
9.   Unplug the air supply blower.
 
10.  If unused boats are still behind the building, strap and stake to the ground.
 
11.  Vessels at dock:
      Have all batteries fully charged.
      Test bilge pumps.
      Add additional fenders and dock lines.
      Bring in power cable off of the dock.
      Lower antenna secure dive ladder.

12.  Place moveable electronic equipment and computers to higher location in the building and cover with plastic.